## Slide 1: Proposed Instrumentation Plans

## Slide 2
32 Acclerometers:
20 vertically oriented accels
6 transversely oriented accels
6 longitudinally oriented accels
Span 7
Span 8
Acceleration Instrumentation Plan

## Slide 3
6 Strain Gauges:
2 Locations
1 centered on bottom flange
2 installed on web
Sampled at 100 Hz to capture dynamic effects
40% Span
Mid-span
Span 7
Strain Gauge Plan. Objectives:
Estimate “Dynamic Amplification Factor”
Identify location of maximum response (controlling shape)
14’

## Slide 4
6 Strain Gauges:
2 Locations
Bottom flange locations capture out of plane
Web locations locate neutral axis and separate axial from bending force
Sampled at 100 Hz to capture dynamic effects
Span 7
Strain Gauge Plan. Objectives:
Determine how pier is being driven transversely