## Slide 1: I76 Vibration Study
2 Stage Test
1st Phase – Longitudinal Survey
  Instrument Piers
  Lateral Acceleration
  Short Duration
2nd Phase – Monitoring Section
  Instrument Representative Section
  Acceleration of Superstructure
  Characterize Structure

## Slide 2
32 Acclerometers:
20 vertically oriented accels
6 transversely oriented accels
6 longitudinally oriented accels
Span 7
Span 8
Acceleration Instrumentation Plan

## Slide 3
6 Strain Gauges:
2 Locations
1 centered on bottom flange
2 installed on web
Sampled at 100 Hz to capture dynamic effects
40% Span
Mid-span
Span 7
Strain Gauge Plan. Objectives:
Estimate “Dynamic Amplification Factor”
Identify location of maximum response (controlling shape)
14’

## Slide 4
6 Strain Gauges:
2 Locations
Bottom flange locations capture out of plane
Web locations locate neutral axis and separate axial from bending force
Sampled at 100 Hz to capture dynamic effects
Span 7
Strain Gauge Plan. Objectives:
Determine how pier is being driven transversely

## Slide 6: Phase 1
Span 3
Span 4
Span 5
Span 6
Span 7
Span 8
Span 9
Span 10
G2
G3
G4
G5
G6
G7
G8
G9
G10
Test Design to Avoid Traffic Control
4 Continuous Sections of interest
Accel. placed on side of piers (lateral)
Access provided with ladders
Record vibration for several hours
Determine “liveliest” section
If negligible difference:
  Choose section most conducive to testing
Otherwise choose “liveliest” span

## Slide 7: Phase 2
Extended Vibration Study
32 Accelerometers on Girders
Record for several days
Capture vibration characteristics
Monitor vibration amplitude
Correlate with traffic via video
St-ID with FE modeling
Identify possible methods to mitigate vibration discernable by public

## Slide 8: I76 Requirements
Phase 1:
Complete construction documents, inspection reports, CAD drawings
Phase 2:
Aerial Lift
  2 days install
  1 day breakdown
Power
Video camera capturing traffic
60 Feet Minimum

## Slide 9
THMPR